Kernel Probes for ARM
Quentin Barnes
q.barnes@motorola.com
Motorola - Mobile Devices
April 17, 2007

---
Overview
Introduction to kernel probes
How kernel probes work
The classic kprobe model and 'boosting'
Difficulties with the classic model and ARM
New approach used for ARM
  - Details of implementation
  - Cost and Performance
Wrap-up

---
Kernel Probes Introduction
New with 2.6.9-rc2 kernels
  - Currently: avr32, i386, x86_64, ia64, powerpc, sparc64, s390
Allows dynamic breakpoints (registered at runtime) to be placed most anywhere in kernel
Breakpoint transfers control to user specified handlers, executes the instruction, and returns
User handlers often used to aid debugging or collect performance data
Can be relatively low overhead

---
Types of Kernel Probes
Kprobes - “Kernel Probes”
  - Places breakpoint at symbol plus offset or address
Jprobes - “Jumper Probes”
  - Insert function call ahead of probed function
Kretprobes - “Return Probes”
  - Probe function's return
Djprobes - “Dynamic Jump Probes”
  - Future direction: Kprobe-like, uses a jump instruction rather than a breakpoint

---
How Do Kprobes Work?
Places a breakpoint instruction most anywhere
  - On ARM, uses an undefined instruction
May register optional user pre-, post-, break, and fault handlers
  - User handlers can do most things except block
More than one Kprobe allowed at one address
  - Not so for Jprobes and Kretprobes

---
'Classic' Kprobes Model

---
Kprobes Registration & Prep
Do symbol lookup, if necessary
Validate address
Record probe and address for hash lookup
Save instruction at address and replace it with a breakpoint instruction
Allocate and initialize instruction slot
Do additional architecture specific initialization

---
Executing a Kprobe

---
Issues with Classic Model
High execution overhead - two exceptions and four full context switches
Holds interrupts disabled through entire length
  - Some re-enable though resulting in possible unbounded recursion, unpredictable behavior, and skipped user handlers

---
Performance Gain – 'Boosting'
Take one exception instead of two
Boosting short-circuits the second exception for pre-determined instructions by jumping directly back after execution

---
Boosting Limitations
Limited to only 'boostable' instructions
  - No conditional jumps and no reserved or special instructions
Non-boostable instructions still run classic way (using two exceptions)
Use of post-handlers disable boosting still running classic way
Garbage collector

---
Boosting's Garbage Collector
Boosting holds lock on instruction slot even after execution completes
Garbage collector needed to clean up unused locks
When kernel preemption is enabled, garbage collector disables all interrupts and freezes all kernel threads across all CPUs simultaneously to run its O(n) time algorithm

---
Difficulties with Kprobes & ARM
No single-stepping supported in the processor
  - Single-stepping causes the processor to trigger an exception after completing the current instruction
No Next-PC register
  - The Next-PC register steps the processor to the “next” address after completing the current instruction

---
ARM Difficulties (cont.)
So no way to regain control of the ARM processor after executing instructions that alter the PC without decoding, detecting, and handling all instructions that can write the PC
No way to give correct results for instructions that read the PC without decoding, detecting, and handling
Once you've gone that far already, it's not that much further to a new approach

---
New Kprobes Approach

---
New Kprobes Goals
Do as much prep work as possible during registration of a kprobe to reduce its execution overhead
Complete the kprobe'd instruction and all its side-effects before returning from first (and only) exception
Provide consistent execution and behavior
Don't hold any locks longer than necessary

---
New Kprobes Advantages
Fully self-contained within arch, no changes to generic Kprobes code needed
Can work for all instructions, not just some
Always works, regardless of post-handlers
No second exception ever, so all that support code and additional logic goes away
No locks left dangling – so no headaches and no garbage collector

---
Advantages (cont.)
Interrupts disabled throughout single exception
  - No unbounded recursion
  - User handlers guaranteed to be called unless a handler itself triggers recursion by having a kprobe
Very light-weight
  - Small code size
  - Low execution overhead
MP and Preemptive (CONFIG_PREEMPT) clean

---
How Does *insn_handler() Work?
At registration time:
  - Depending on the form of the kprobe'd instruction, an instruction execution handler is assigned
  - Registers used by the instruction are recoded to use the registers the instruction handler expects
  - Modified instruction or condition code test instruction saved to instruction slot
Two groups of instruction handlers - ones that execute a modified form and ones that resolve the instruction in straight C code
  - C-only ones are for instructions that write the PC

---
Instruction Handler: Example 1
Kprobe'd instruction - “blne addr”
Modified instruction in slot - “movne r0, #1”
Handler assigned - simulate_bbl()
  - 25 total instructions

---
simulate_bbl()
All in C since “bl” writes to the PC
Handles both “b” (branch) & “bl” (branch & link)
Could have been two handlers

---
insnslot_1arg_rflags()

---
insnslot_1arg_rwflags()

---
Instruction Handler: Example 2
Kprobe'd instruction - “add r3,r6, #7”
Modified instruction - “add r0, r0, #7”
Handler assigned – emulate_alu_imm_rflags()
  - 19 total instructions

---
emulate_alu_imm_rflags()

---
Isn't It Expensive?
Twenty-seven instruction handlers (5 sim + 22 emul) cover virtually all ARM instructions
Most instruction handlers compile down to just 10-40 instructions
The ARM Kprobes is 6.6KB of code
With no second exception ever and no boosting, all that support code is tossed away

---
Overhead Performance
Overhead results on PXA270@364.00MHz
  - Kprobe: 1.21us
  - Jprobe: 3.11us
  - Kretprobe: 3.40us
  - Kprobe + Kretprobe: 3.81us
  - Jprobe + Kretprobe: 5.86us
Measured with Jim Keniston's kprobe overhead testing software with defaults (iter=5000000, handler=1)

---
So What's the Catch?
Uses a lot of decode decision paths and some handlers infrequently used, so needs extensive testing and chance of latent bugs
Technique is easiest for RISC and orthogonal instruction sets, but could be harder for others

---
State of the Port
Kprobes, Kretprobes, and Jprobes complete and all working
Some bugs still running around
Some rare and unusual instructions not supported – ones that change CPSR state
Patches for 2.6.20.4 kernel released to Systemtap/Kprobes mailing list on 4/11/07

---
What's Left
Shakeout of approach and code
Test suite to test all decode paths and instruction execution handlers
Integrate into ARM Linux and kernel.org trees
Finish port of Systemtap's runtime and test suite to ARM and modify Systemtap to support cross-compiles
Djprobe version

---
What's Left? (cont.)
Remember for the new Kprobes I said one of the goals was to do as much prep work as possible? I'm not quite doing that yet...
Use larger instruction slots, do more at registration and less at runtime:

---
Systemtap
User space front end to Kprobes
Simple command line interface and scripting language
Does it all – compiles script to C code, builds, loads, and runs the kernel module

---
URLs
Systemtap:
  - Home: http://sourceware.org/systemtap/
  - Mailing list: http://sourceware.org/ml/systemtap/
Motorola Open Source
  - http://opensource.motorola.com/

---
Questions?